## Slide 1: Robotic Sensor Systems (RSS) Project
Group Number 12
Prof. Dr.-Ing. Robert Schmitt
Laboratory for Machine Tools and Production Engineering WZL, RWTH Aachen University
Winter Semester 2025/26

## Slide 2: Project Structure
ESP32
UDP
IMU
IR
Encoder
SERVO
arm_servoing
servo_rviz
wifi_sensor_bridge
Teleoperation of Simulated Kinova Gen3 Robot
Control 7-DOF simulated robot in real time using wearable sensors, ROS2, and MoveIt2 Servo.

## Slide 3: Sensor Mapping
Components and Mapping:
ESP32 →
IMU – I2C communication
IR – Digital reading
Encoder – Hardware interrupts for dial and digital read for button
IMU MPU6050 sensor →
  Calculate Roll, Pitch, Yaw angles
  Control node calculates velocities vx, vy and vz respectively.
  Control node generates Twist Commands for moveit_servo.
  Yaw is used to control opening and closing of gripper.
Rotary Encoder sensor →
  Rotary knob is used to switch between 3 control modes (TCP Translation Control (w.r.t. base_link), TCP Orientation Control (w.r.t. end_effector_link). Gripper open/close control.)
  The button has 2 modes – toggle between master RUN and master OFF. Long press (> 1 sec) triggers Homing for the robotic arm. (joint_trajectory_controller/joint_trajectory) [Useful in near singularity conditions].
IR Sensor →
  The IR sensor is used as an Emergency Stop.
  No commands from IMU are accepted when the proximity of iR sensor is triggered.

## Slide 4: ROS2 Nodes
wifi_sensor_bridge:
  This node accepts the sensor data from esp32 on udp port 5000 and pusblishes it to ROS topics /wifi/imu and /wifi/enc.
arm_servoing:
  This is the main controller node that accepts the sensor data from the topics /wifi/imu and /wifi/enc.
  The encoder data is then used to define control modes.
  The IMU RPY data is used to calculate vx, vy & vz.
moveit_servo:
  moveit2 package was cloned from the movit github repo and built in overlay_ws to enable /moveit_servo and its complimentary services and topics.
servo_rviz:
  The gen3_servo_config.yaml file contains the important parameters for the servo controller. It defines parameters like move_group_name, singularity_threshold, planning_frame, etc for our kenova gen3 robotic arm.
  The servo_rviz.launch.py launches the rviz sim and all the nodes required to make the control pipeline work.

## Slide 5: GUI
We have added a GUI to keep track of –
IMU RPY values
Velocities
Run Mode
Control Mode
Reference Frame
Gripper Position
Homing Status
Emergency Stop Status

## Slide 6
THANK YOU !